## Slide 1: 5G challenges in shared spectrum
Unlicensed band - ISM (NII 5GHz) band

## Slide 2: Spectrum Sharing
Situation
meeting growing spectrum demand is constrained by lack of vacant spectrum.
high price associated with re-allocating spectrum to new uses (cost, delays and the occasional need to switch off incumbent users).
FCC policy
TVWS – shared band
2.4GHz & 5GHz ISM unlicensed band
3550-3650GHz - Enabling Innovative Small Cell

## Slide 3: Features in shared band
Incumbents
Licensed User
DoD(department of defense) radar
FSS(fixed satellite station)
Coexistence
General Authorized Users

## Slide 4: WiMax 802.16 , WiFi 802.11a
OFDM based systems are very sensitive to symbol timing errors
Different media access control.
IEEE 802.16 has a centralized architecture provided by a central Base Station (BS) with associated Subscriber Stations(SS).
802.16 offers guaranteed multimedia QoS.

## Slide 5: parameters
802.16 - Contention Slot Duration for BW Requests 2 Symbols 27.78 μs
802.16 - Contention Slot Duration for Initial Ranging 10 Symbols 138.9 μs
802.11 - DIFS length 34 μs, backoff slot 9 μs
802.11 – data package transmission 2 ms

## Slide 6: IEEE 802.16 MAC frame

## Slide 7: IEEE 802.11 MAC frame

## Slide 8: Collisions

## Slide 9: Conclusion
Guarantee of QoS in 802.16 takes extra mechanisms.
Blocking 802.11(a) out of the medium is proposed in reference paper.
From the perspective of 802.11a, the proposed method can be regarded as unfair.
Better approach: Hybrid Coordinator